## Slide 1
FYP ENGINEERING PORTFOLIO
From neural intention to robotic assistance
A detailed record of the P300/EEG, Transformer, vision and robotic systems behind Project Flamescion.
PROJECT FLAMESCION
FYP ENGINEERING PORTFOLIO / 01

## Slide 2
CONTENTS
Contents
FYP ENGINEERING PORTFOLIO / 02
The portfolio follows the path from user intention to physical action.
01
Research question and system framing
02
P300 acquisition and physiological evidence
03
Transformer decoder and decision logic
04
Evaluation design and results
05
Vision, robotics and supporting systems
06
Engineering direction

## Slide 3
RESEARCH FOCUS
The FYP in one view
FYP ENGINEERING PORTFOLIO / 03
The FYP asks whether a user’s attention can select a physical object through a non-invasive EEG interaction system.
The user provides one discrete intention: which object to select. The machine handles scene understanding, P300 evidence accumulation, object identity, localisation and robotic motion.
APPLICATION METRIC
Final object selection, not single-flash classification.

## Slide 4
RESEARCH QUESTION
From attention to action
FYP ENGINEERING PORTFOLIO / 04
The research translates a P300 response from attended object labels into a verified target for a robotic system.
The system is designed as shared control. Neural activity provides the high-level intention, while the machine handles the visual scene, repeated evidence, calibration and physical execution.
SHARED CONTROL
Brain chooses. Machine executes.

## Slide 5
SYSTEM ARCHITECTURE
End-to-end system architecture
FYP ENGINEERING PORTFOLIO / 05
01
Scene
Frozen frame and vision model return four candidate objects.
→
02
EEG
36 flashes create 32-channel EEG epochs.
→
03
Decision
Transformer scores target evidence and selects one object.
→
04
Robot
Identity check, calibration, preview and arm command.
The system keeps a stable item identity from the vision label to the final robot target.

## Slide 6
P300 ACQUISITION
P300 acquisition protocol
FYP ENGINEERING PORTFOLIO / 06
EEG CHANNELS
32 channels
EMOTIV FLEX recording
SAMPLING RATE
128 Hz
Session-level recording
EPOCH WINDOW
−0.2 s to +0.8 s
129 samples per epoch
FLASH PROTOCOL
36 flashes
4 objects × 9 repetitions
STIMULUS TASK
One attended label
Candidate names are flashed
SELECTION UNIT
One object
Evidence is accumulated by object

## Slide 7
PHYSIOLOGICAL EVIDENCE
ERP evidence
FYP ENGINEERING PORTFOLIO / 07
Representative P7, session 5 and Fz ERP traces show target and non-target responses separating in the expected P300 window.
This physiological separation shows that the session contains task-related ERP evidence that can support decoding. It is presented as representative session evidence rather than a universal result for every recording.
WHY IT MATTERS
The decoder receives a measurable attention-related signal.

## Slide 8
SIGNAL ROUTE
From EEG epoch to decision
FYP ENGINEERING PORTFOLIO / 08
Each flash creates a time-locked EEG epoch. The decoder scores target evidence, and object-level accumulation combines repeated flashes before a final choice.
This keeps the decision tied to an object rather than treating one isolated flash score as the final interaction output. The object identifier then continues into the robotic control route.
DECISION UNIT
One selected object.

## Slide 9
NEURAL DECODER
Transformer-based P300 decoder
FYP ENGINEERING PORTFOLIO / 09
INPUT
129 × 32
Time samples × EEG channels
PROJECTION
192
Model representation dimension
ENCODER
3 layers
4 attention heads in each layer
FEED-FORWARD
1024
GELU activation with 0.20 dropout
OUTPUT
2 logits
Target and non-target margin
The route starts from a base checkpoint trained on 24,091 public epochs, then adapts to the recorded participant route.

## Slide 10
EVALUATION DESIGN
Evaluation design
FYP ENGINEERING PORTFOLIO / 10
Session-level splits
Separate recordings by session so epochs from one recording do not appear on both sides of a split.
Participant-specific route
Each participant keeps an independent adaptation route and normalizer.
Validation-only search
Adaptive choices use validation evidence, while diagnostic test fields remain hidden during selection.
Application metric first
Object-selection accuracy ranks the system; flash F1 explains signal-level behaviour.

## Slide 11
EVALUATION EVIDENCE
Evidence by evaluation layer
FYP ENGINEERING PORTFOLIO / 11
PUBLIC BASE MODEL
71.07% target F1
Architecture-development evidence
STRONGEST SAVED ROUTE
75 / 83.33
Validation / held-out result
LIVE B-V2 SELECTION
35 / 49
71.43% labelled bursts
V2 ARM COMMAND
48 / 68
Command completion record
Each result answers a different question: decoder behaviour, saved-route evaluation, live selection, or command execution.

## Slide 12
ROBOTIC EXECUTION
From selection to physical action
FYP ENGINEERING PORTFOLIO / 12
01
Frozen frame
The vision layer holds one frame before candidate objects are selected.
02
Object identity
The selected label stays attached to one item ID across the decision and movement steps.
03
Calibration
A calibration mat and AprilTags align the target position with the robot workspace.
04
Reachability and preview
The control path checks the planned movement before execution.
05
DOFBOT command
The robot environment receives the verified target and performs the motion routine.

## Slide 13
R-ARM BRANCH
Custom robotic-arm work
FYP ENGINEERING PORTFOLIO / 13
The R-Arm branch combines CAD, ESP32 control, visual picking and motion routines for a separate custom hardware route.
The branch provides a parallel test environment for the FYP direction: a physical arm, visual target handling and low-level motion control connected through a defined software path.
SYSTEM ROLE
Custom-arm development and physical-control testing.

## Slide 14
ROBOTIC GROUNDWORK
TENG-based adaptive robotic grip
FYP ENGINEERING PORTFOLIO / 14
A tactile-feedback grip prototype adjusts the closing action to a pressure target associated with the detected object.
Human hand
1.38 N
Mouse
1.24 N
Pen
1.09 N
Bottle
0.79 N
Object identity → target hardness → tactile feedback → stop or release

## Slide 15
ALTERNATIVE INTERACTION
Iris-based intent selection
FYP ENGINEERING PORTFOLIO / 15
A gaze-and-confirmation module can replace the EEG input while preserving the rest of the robotic pipeline.
The camera and vision model keep their object labels, the selection module produces one target ID, and the downstream state machine and arm-control path can receive the same decision format.
PURPOSE
A hands-free selection route for a robotic-arm demonstration.

## Slide 16
SUPPORTING SOFTWARE
Tools around the core system
FYP ENGINEERING PORTFOLIO / 16
The FYP work includes VLM utilities, interface components, collection tools, datasets and test material that support the main EEG-to-robot pathway.
These components support the same direction: collect controlled evidence, decode one selection, preserve object identity and send a verified target to a robot-control environment.
ENGINEERING SCOPE
EEG, Transformer, vision, interface and robot control.

## Slide 17
ENGINEERING DIRECTION
Current technical focus
FYP ENGINEERING PORTFOLIO / 17
Reliability versus latency
Nine repetitions per object provide repeated evidence, but each repetition adds selection time.
Cross-session behaviour
The route must keep the same decision quality across different recording sessions.
Decision layer
Confidence-aware stopping can use only the evidence needed before the system acts.
Physical feedback
Neural selection, sensing and robot motion need one safety-aware control path.
The next target is a lower-latency neural decision that remains useful for real robotic assistance.

## Slide 18
SUMMARY
FYP system in one view
FYP ENGINEERING PORTFOLIO / 18
01
Intention
A user attends to one visible object label.
02
Evidence
P300 EEG epochs pass through a Transformer decoder.
03
Decision
Repeated flash evidence selects one object.
04
Action
Vision identity, calibration and robot control execute the physical step.
Project Flamescion connects neural intention, machine decoding, scene understanding and robotic action in one engineering system.